## Slide 1
Identifying Partners/Licensees
SIMPLE AND NOVEL RETROFITABLE RETRACTABLE NON-TORQUE AIR SUSPENSION SYSTEM
Delhi . Mumbai . Bangalore . Pune . Indore

## Slide 2
Concerns lying with the known air suspension systems :
    Mobility v/s stability
    Generally heavy
    Expensive to manufacture
    Low roll stability
    Frame rise
    Driveline vibrations
    Non-reactive
BACKGROUND
Notes: 2

## Slide 3
Issues associated with the multi axle vehicles :
    High fuel consumption
    Road holding quality
    Poor tire
    Suspension parts life
    Low manoeuvrability
    Difficult cornering
Concerns lying with hydraulically liftable auxiliary axles :
    Heavy construction
    Relatively expensive
    High operating cost
    High shock forces
    Side thrust force
BACKGROUND (CONTINUED)

## Slide 4
    New optimized hanger brackets mounted to the LH & RH Frames.
    Longitudinally extended arms connected to the hanger brackets at leading ends, extend parallel to the frame.
    Trailing ends of the arms interconnected by a cross bar extending laterally, also parallel to the vehicle axle centre line.
    Ride air bellows - one end connected to top of the arms trailing end and the other end connected to frame bottom.
    Arms having axle pivot bore in between the ends with an axle clamp assembly to connect to axles.
PROPOSED TECHNOLOGY

## Slide 5
    Torque rod or control rod assembly connected at the centre of the axle housing and the frame.
    Together with arms, control rod assembly and brackets forms a parallelogram configuration.
    Arms form the lower link and the control rod forms the upper link.
    Pneumatically operated mechanism connected at the cross bar and the frame to lift the auxiliary axles.
    Pneumatic mechanism consists of a lift air bellow, mounting brackets, U-bolts and fasteners.
    Ride air bellows and lift air bellows works as an air suspension system.
PROPOSED TECHNOLOGY

## Slide 6
    Novel joint between cross bar and trailing ends of arms
    Novel bottom bracket for ride air bellow
    Novel I- shaped cross section
    Bump stop feature
    Shock damper mounting features
    Rebound stop inside the lift air bellows
PROPOSED TECHNOLOGY- NOVEL FEATURES

## Slide 7
Retro-fitable & Retractable
Operates on normally available compressed air in the vehicle
Modification of existing components not required
Low cost, low maintenance lifting device
Operates by simple control switch
Auxiliary axle(s) of MAV’s get lifted by about 120mm-150mm
ADVANTAGES

## Slide 8
Air Suspension can be converted into lift-able suspension by adding the lifting mechanism
Air Suspension System
Liftable Mechanism
Air Suspension system in vehicle
Air Suspension With liftable mechanism
ILLUSTRATION

## Slide 9
Patent no: US7722064
Optimized Design- Bracket
New Concept –Arm Design
New Concept –Cross bar Design
New Concept –Arm, Cross bar & Air bellow
bottom bracket connection
Comparison with the existing Design

## Slide 10
New Concept –Torque rod
Simplified Concept – Axle stop
New Concept –Ride air bellow bottom Bracket

## Slide 11
New Concept – Lift-able system Design

## Slide 12
New & Optimized Concept – Brackets Design
Ride Air Bellow Bracket for Lifting mechanism
Lift Air Bellow Top Bracket
Lift Air Bellow Bottom Bracket

## Slide 13: PATENT/IP STATUS
Application Number: 2460/CHE/2014
Application Status: Published on 15/01/2016
Date of filing: 19/05/2014

## Slide 14
EXPECTATIONS
Inventor/Applicant of the instant technology is interested in Out-Licensing or Selling the Technology and Assigning the Patent Rights to one or more of
  Truck Manufacturers
  Trailer manufacturers
  Bus manufacturers
  Suspension manufacturers

## Slide 15
Contact Details
Noida (NCR) Office
E-13, UPSIDC Site-IV, Behind Grand
Venice, Greater
Noida, 201308
Contact Person: Tarun Khurana
Contact No.: +91-120-4296878/2399010-11
E-Mail: iiprd@iiprd.com, info@khuranaandkhurana.com
Website: www.iiprd.com, www.khuranaandkhurana.com
DELHI. MUMBAI. BANGLORE. PUNE. INDORE. CALIFORNIA