## Slide 1
SAMPLE LANDSCAPE STUDY
NMC Lithium-ion Batteries for Electric Vehicles

## Slide 2: Contents
Introduction to NMC Lithium-ion Batteries
Growth Prospects of NMC Lithium-ion Batteries
Key Developments – Lithium-ion Batteries Electrode Materials
Objectives of the Landscape Study
Trend Analysis and Graphical Representation
Key Technology Trends
Patent Portfolio Analysis – Technological Dissection of Patent Portfolio and Analysis of Key Granted Patents
Analysis of Key Granted Patents Assigned to Educational Institutes and Other Companies
Appendix A – Sources
Appendix B – Definition of IPC Classes

## Slide 3: Introduction to NMC Lithium-ion Batteries
Lithium-ion batteries (LIB) have become an essential energy storage since their development in the early 1990’s for a wide range of applications including automobiles, digital electronics and other energy storage systems.
LIB are projected to become the most popular battery for electric vehicles (e-mobility) for their potential to reduce greenhouse emissions and decrease dependence on gasoline/oil. It is estimated that by 2020, more than half of new vehicle sales will likely be consist of electric vehicle (EV), hybrid-electric vehicle (HEV), and all-electric models.
Industry is refocusing of LIB applications from consumer applications to e-mobility, which needs different battery characteristics and one example is in the development of new cathode materials.
Today, the largest cathode material segment is LiNiMnCoO2 (NMC) which better matches the needs of huge e-mobility market and also of most other applications.
NMC has established a universal Li ion technology with large variety of applications covered for great future potential due to its high energy density and thermal stability when compared with other cathode materials.
Batteries should have a right balance between specific energy, storage capacity, cost, lifetime, recharge time, and safety to achieve commercial success for EVs - NMC is the one which can provide all the above properties.
For sources of information, please refer to Appendix 1

## Slide 4: Growth Prospects of NMC Lithium-ion Batteries
The global LIB market is expected to reach USD 93.1 billion by 2025, growing at a CAGR of 17.0% attributing to the increased usage of lithium-ion batteries in electric vehicles.
The Boston Consulting Group (BCG) estimated that by 2030, Mild Hybrid Electric Vehicles (MHEVs) will represent 15% of the global automotive market while Hybrid & Battery Electric Vehicles (HEVs) will represent 13% and 14% respectively.
While other types of LIBs will continue to retain considerable market share in the short term, NMC lithium-ion batteries expected to dominate the automobile (e-mobility) segment with 51% of the global cathode material market by 2022, driven by the increasing demand for electrical vehicle applications.
Increasing adoption of NMC in power tools, e-bikes and other electric powertrains on account of its higher energy density, lower cost, and longer cycle life will fuel its demand over the forecast period. NMC offers overall performance and excels on specific energy and possess high capacity and high power.
LG Chemicals, Johnson Controls, Hitachi, and Toyota Motor are some of the main IP players mentioned in the report - The main IP players are not always main market players.
It is a critical time to understand the global competitive environment of NMC lithium-ion batteries from a patent perspective and in-depth patent analysis of key technologies and players can help anticipate changes, detect business opportunities, mitigate risks and make strategic decisions to strengthen one’s market position and maximize return on one’s IP portfolio.
For sources of information, please refer to Appendix 1

## Slide 5: Key Developments – Lithium-ion Batteries Electrode materials
Lithium Nickel Cobalt Aluminum Oxide cathode was discovered
1991
Patents were filed for Nickel Manganese Cobalt (NMC) cathodes
Sony commercialized first Li ion battery -uses Lithium Cobalt Oxide as cathode material and coke as anode material
1999
2000
Lithium Manganese Oxide (LMO) was commercialized and Lithium iron phosphate (LFP) was discovered
1996
Graphite used as anode
1997
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
2004
2017
Bosch introduced new 48 V Li-ion battery (NMC/Graphite) for mild hybrids
First Li battery powered car (Tesla’s ‘Roadster’) was introduced
For sources of information, please refer to Appendix 1

## Slide 6: Objectives of the Landscape Study
To understand technology and prepare patent landscape
To understand major patent holders, geographical distribution of patents, top sub-technologies based on IPC codes
Analysis of patent filing trends over the years, top assignees, top patent classifications, among others
To conduct Patent Portfolio based study of patents relating to core focus area of NMC as cathode material for Lithium ion batteries in the patents/applications
Assumptions:
Report provides patent analysis for NMC Lithium-ion batteries for EVs market, which includes different types of NMC cathode materials used in combination with different anode materials and advance technology based patents.
The landscape study focuses on patents pertaining to NMC cathode materials published between 2008-2018.
For sources of information, please refer to Appendix 1

## Slide 7: Trend Analysis and Graphical Representation
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 8: Filing Trends – Last 10 Years
Chart: 
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 3 | 6 | 9 | 15 | 22 | 14 | 23 | 34 | 37 | 27 | 11
Insights
Global patent filing trend analysis shows a overall rise in the number of patent applications filed during the last 10 years. There is significant rise in the no. of patents filed from the year 2014 onwards with highest filing in the year 2015-2016. Maximum number of patent applications were filed from KR, followed by CN and JP jurisdictions.
Number of Patent Families
Application Year
Chart: 
| KR | CN | JP | US | DE | EP | WO
 | 57 | 55 | 38 | 31 | 10 | 5 | 5

## Slide 9: Publication Trends - Last 10 Years
Insights
# Graphs were prepared based on the analysis of application year for the priority country member
Global patent publication trend presents a overall rise in the number of publications during last 10 years with its peak during 2017-18, which suggests significant filing during 2015-2016. Total number of patents published in 2018 may increase till the end of the year.
Chart: 
| 2008 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 1 | 5 | 2 | 16 | 16 | 14 | 17 | 33 | 41 | 56
Number of Patent Families
Publication Year

## Slide 10: Top Assignee
LG Chemical Ltd is the leading patent applicant in NMC lithium-ion batteries technology, followed by Johnson Controls Tech and Hitachi.
Insights
# Graph was prepared based on the analysis of application year for published applications (based on the representative family numbers)
Chart: 

 | 43 | 12 | 9 | 8 | 7 | 7 | 6 | 5 | 5 | 4 | 4
Assignee
No of patent families

## Slide 11: Top International Patent Classifications (IPCs)
Maximum number of applications filed during 2008-2018 corresponds to IPC class H01M relating to ‘Process or Means eg. Batteries for the Direct Conversion of Chemical into Electric Energy’. Amongst applications filed in H01M, majority of the applications were filed in technology of sub-class H01M 4/505 which relates to ‘Selection of substances as active materials, active masses, active liquids of inorganic oxides or hydroxides of nickel, cobalt or iron of mixed oxides or hydroxides containing iron, cobalt or nickel for inserting or intercalating light metals’.
Insights
# For IPC sub-class definitions please refer to Appendix 2.
Chart: 
Chart: 
| H01M | Others
 | 189 | 11
Chart: 
| H01M0004505 | H01M000436 | H01M00100525 | H01M0010052 | H01M0004525 | H01M000462 | H01M00100585 | H01M000413 | H01M0004131 | Others
 | 29 | 22 | 20 | 14 | 11 | 9 | 6 | 6 | 6 | 66

## Slide 12
Geographic Origin of Innovation
Insights
Analysis of Geographic Origin of Innovation (i.e. Priority Country) demonstrates that maximum number of innovations originated from KR followed by CN , JP and US jurisdictions.
# The graph representing Geographic origin of innovation was prepared based on the analysis of priority country
Jurisdiction
Number of Patent Families
Chart: 
| KR | CN | JP | US | DE | EP | WO
 | 57 | 55 | 38 | 31 | 10 | 5 | 5

## Slide 13: Key Technological Trends
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 14: TYPES OF CATHODE AND ANODE MATERIAL
Insights
Highest percentage of applications (62%) were focused on unmodified NMC cathode materials and (52%) of Graphite anode materials for lithium-ion battery applications in EVs. 17% of cathode material patents are related to mixture of NMC material with other active materials while 14% of anode material patents relates to LTO.
Chart: Negative Electrode (Anode) Material
| Graphite | LTO | Li related | Si containing | Others/Generic
 | 112 | 30 | 23 | 15 | 35
Chart: 
| Unmodified NMC | Modified NMC | Coated NMC | Mixed with other active materials
 | 131 | 26 | 19 | 36

## Slide 15
Chart: Anode Materials Vs Unmodified Cathode
| Graphite/Carbon | Li Metal | Li Containing | Si Containing | Generic/Others
 | 80 | 10 | 23 | 9 | 24
Graphite/Carbon
58%
Chart: Anode Materials Vs Modified NMC
| Graphite/Carbon | Li Metal | Li Containing | Si Containing | Generic/Others
 | 13 | 3 | 4 | 2 | 5
Chart: Anode Materials Vs Coated NMC Cathode
| Graphite/Carbon | Li Metal | Li Containing | Si Containing | Generic/Others
 | 7 | 3 | 2 | 2 | 2
Chart: Anode Materials Vs NMC Mixed with Others
| Graphite/Carbon | Li Metal | Li Containing | Si Containing | Generic/Others
 | 23 | 2 | 7 | 3 | 7
ANODE MATERIALS Vs NMC CATHODE MATERIALS

## Slide 16: Patent Portfolio Analysis
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 17
Patent Portfolio Analysis – LG Chem Ltd
Company Profile
Positive Electrode Material Dissection
LG Chemical Ltd is one of the leading global companies in chemical industry head quartered in Korea.
The company has built the global network for production, sales and R&D not only in Korea but also in main bases across the world and has provided globally competitive products including ABS, polarizers and EV battery cells, raising its global position as a material supplier.
Chart: 
| Graphite/Carbon | Li Metal | Li Containing | Si Containing | Generic/Others
 | 21 | 2 | 5 | 1 | 13
Negative Electrode Material Dissection
Chart: 
| Unmodified NMC | Modified/Doped NMC | Coated NMC | NMC mixed with other Active Materials
 | 9 | 7 | 7 | 20

## Slide 18
US8981037B2
PEF used in preparation of a polyester resin
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
Patent No. | Novel Features
KR101171734B1 | The invention relates to a lithium-nickel-Manganese-cobalt oxide (NMC) where the content of the nickel is 40% or more and the amount of the Li-containing impurities remaining on the surface of the cobalt oxide positive electrode, characterized in that not more than 0.2% active material.
JP06007431B2 | The invention disclosed a NMC based cathode active material contains fluorine, and at least one metal selected from a group consisting of Mg, Ti, Zr, Al and Fe as well as sulfur (S) . 50 to 99.9% of a total weight of fluorine contained in the active material is present on a surface of the lithium transition metal oxide and content of the sulfur ranges from 0.005 to 5 wt. % relative to a total weight of the NMC. lithium nickel-manganese-cobalt oxide having a nickel content of 40 to 70% relative to a total amount of nickel-manganese-cobalt. The above described cathode active material showed improved properties at high voltages.
Key Patents
Patent Portfolio Analysis – LG Chem Ltd

## Slide 19
Patent No. | Novel Features
US9118075B2 | The invention disclosed NMC based cathode active material wherein the lithium nickel-manganese-cobalt oxide has nickel content of at least 40% among overall transition metals and is coated with lithium phosphate solid compound at a surface thereof. A lithium secondary battery having the disclosed cathode active material has advantages of not deteriorating electrical conductivity while maintaining high temperature stability, so as to efficiently provide high charge capacity.
US8329339B2 | The invention disclosed a polymer coated lithium nickel manganese cobalt oxide (NMC) cathode active material represented by Formula LixNiyMncCOdO2 wherein c+d=1−y, provided 0.05≦c≦0.4 and 0.1≦d≦0.4 wherein the nickel content of at least 40% among overall transition metals. The polymer that used for coating having a melting point of 80 to 300° C. and reside at a surface thereof. A lithium secondary battery having the disclosed cathode active material has advantages of not deteriorating electrical conductivity while maintaining high temperature stability, so as to efficiently provide high charge capacity.
Patent Portfolio Analysis – LG Chem Ltd

## Slide 20
Patent No. | Novel Features
US8110308B2 | The invention provided a lithium secondary battery having excellent low-temperature power output characteristics where the cathode comprises a mixture of lithium manganese oxide (LMO) and a lithium nickel-manganese-cobalt composite oxide (NMC) as a cathode active material in combination with a given amount of a lithium metal oxide and/or a lithium metal sulfide anode mix with carbon based anode active material for a lithium secondary battery. The secondary battery can be used as a power source for electric vehicles (EVs) and hybrid electric vehicles (HEVs) that must provide high-power output at low temperatures as well as at room temperature.
US9269951B2 | The invention provides a cathode active material for a lithium secondary battery, comprising a mixture of lithium/manganese spinel oxide (LMO) represented and lithium/nickel/cobalt/manganese oxide (NMC) wherein the mixing ratio of the LMO to NMC is in the range of 10:90 to 90:10 (w/w) and the cathode active material exhibits the life characteristics that the capacity at 300 cycles is more than 80% relative to the initial capacity. The high-power lithium secondary battery having a long-term service life and superior safety at both room temperature and high temperature, even after repeated high-current charge and discharge
Patent Portfolio Analysis – LG Chem Ltd

## Slide 21: Patent Portfolio Analysis - Johnson Controls
Chart: 
| Graphite/Carbon | Li Containing | Generic/Others
 | 3 | 2 | 7
Company Profile
Negative Electrode Material Dissection
Johnson Controls is a global diversified technology and multi industrial leader serving a wide range of customers in more than 150 countries.
Johnson Controls offer a range of lithium-ion battery technology for Passenger vehicles, from those with internal combustion engines to fully electric vehicles; Commercial vehicles including heavy-duty trucks and construction vehicles. also recreational vehicles such as golf cars, marine vehicles and motorcycles/power sports vehicles
Chart: 
| Unmodified NMC | Coated NMC
 | 10 | 2
Positive Electrode Material Dissection

## Slide 22: Patent Portfolio Analysis – Johnson Controls
US8981037B2
PEF used in preparation of a polyester resin
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Patent No. | Novel Features
US9446963B2 | The invention disclosed a cathode comprising an active material, wherein the active material comprises both a spray-dried lithium metal oxide (LMO) component and a co-precipitated LMO component, wherein the spray-dried and the co-precipitated LMO components are both lithium nickel manganese cobalt oxide (NMC) materials having the formula LiNi1/3Co1/3Mn1/3O2
US9761862B2 | The invention disclosed a performance of a coated NMC material used in lithium ion-cell . The cathode is layered metal oxide of Lithium Nickel Manganese Cobalt Oxide (NMC) with Ni:Mn:Co ratios of 1:1:1, and is improved by coating the surface with a sulfonyl-containing compound, such as poly(1,4-phenylene ether-ether-sulfone) which inhibits the reactivity of the electrolyte with the oxidized electrode surface while allowing lithium ion conduction.
Key Patents

## Slide 23: Patent Portfolio Analysis – HITACHI
Company Profile
Hitachi supplies lithium-ion batteries with a proven track record for a wide range of vehicle models as well as batteries for plug-in hybrid vehicles and electric vehicles..
The Hitachi's R&D Group is developing battery of "long operating life", "high power", "high energy density", "high durability", "safety", and "low cost" for automotive applications. These batteries are now widely used in hybrid electric small-sized trucks, buses and hybrid railway motorcars.
Chart: 
| Unmodified NMC | Mixed NMC
 | 8 | 1
Chart: 
| Graphite/Carbon | Generic/Others
 | 9 | 1

## Slide 24: Patent Portfolio Analysis – HITACHI
US8981037B2
PEF used in preparation of a polyester resin
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Patent No. | Novel Features
JP05693998B2 | The invention related to Li ion battery includes a positive electrode, a negative electrode, a separator sandwiched between them. The positive active material is nickel-manganese-cobalt composite (NMC) oxide with pore size of 10nm to 1m. The invention described the method of making positive electrode by kneading the binder and solvent with active material and the process helps in decrease the internal resistance and ensure the reactive area of the active material , also preventing the active material from peeling.
JP2016062786A | The invention discloses a lithium nickel manganese cobalt complex oxide positive electrode for a lithium ion secondary battery. The NMC cathode enables the suppression of the increase in battery DC resistance in the event of the temperature rise. The positive electrode also comprises a positive electrode current collector, an underlying layer provided on the positive electrode current collector and including conductive particles, polymer particles, and water-soluble polymer.
Key Patents

## Slide 25: Analysis of Key Granted Patents Assigned to Educational Institutes and Other Companies
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 26: Granted Patents Analysis – Institutes
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent No. | Novel Features
KR1848677B1 Korea Institute of Industrial Technology | The invention relates to a positive electrode composite material lithium nickel cobalt manganese oxide (NCM) for a lithium secondary battery. The positive electrode composite material prepared by using a coprecipitation method and more particularly the positive electrode composite material by using a coprecipitation method complexed with the solid electrolyte to improve the energy efficiency of the battery. The solid electrolyte of the positive electrode composite material including the undoped lithium lanthanum zirconium oxide (lithium lanthanum zirconium oxide, LLZO) or Al-doped lithium lanthanum zirconium oxide(Al doped lithium lanthanum zirconium oxide, and Al doped LLZO).
KR1275260B1 Korea Institute Of Ceramic Engineering And Technology | The invention provides a cathode active material comprises ZnO coated NCM materials for batteries. More particularly, a lithium manganese oxide (LMO) used as a composite material coated with ZnO coated NCM (lithium, nickel, cobalt, manganese oxide) further above, to implement the high- capacity and high-temperature stability at the same time. The weight percent of NCM is characterized in that is 25 to 45 wt.% coated on the surface of ZnO layer.

## Slide 27: Granted Patents Analysis – Other Companies
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent No. | Novel Features
CN102656724B Toyota Motor Co Ltd | The invention provides a method of manufacturing a layered structure lithium nickel cobalt manganese composite oxide (NMC) positive electrode active material for lithium secondary battery. The method involves heating the starting materials of lithium, nickel, cobalt and manganese sources in the pre-baking step at a temperature of pre-calcination, the false calcining temperature was lower than 800 ℃, and exceeds the melting temperature of the lithium supply source. Finally the pre-calcined product obtained in the pre-baking step is heated to the pre-calcination temperature exceeds a step of firing temperature range.
JP6403285B2 Automotive Energy Supply Corp | The invention provides a lithium ion secondary battery including a positive electrode having a layered crystal structure lithium nickel manganese cobalt composite oxide (NMC) as a ppositive electrode active material. The positive electrode active material further comprises lithium-manganese based oxide (LMO). A negative electrode having a negative electrode active material layer disposed on a negative electrode current collector; a separator; and an electrolyte solution. The electrolyte solution contains a disulfonic acid compound as an additive. A mass of the disulfonic acid compound adsorbed on the positive electrode is 1.0 g/m2 or less per unit surface area of the lithium nickel composite oxide.

## Slide 28: Granted Patents Analysis – Other Companies
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent No. | Novel Features
CN104810506B Wanxiang Group Co Ltd | The invention relates to a high-energy density lithium-ion battery. The battery comprising a nickel-cobalt-manganese three yuan cathode material coated positive electrode sheet in combination with silicon carbon nanotube coating form SiO coated negative electrode sheet, separator, electrolyte.
US9698424B2 Bosch Gmbh Robert | The invention provides a cathode unit for a Li ion battery, in which the cathode contains nickel-cobalt-manganese oxide, a salt of an alginic acid, and optionally carbon, or the cathode contains a composite material made of nickel-cobalt-manganese oxide, Li2MnO3, a salt of an alginic acid, and optionally carbon. The patent also described the method of manufacturing the algininate binded NMC cathode units under shear stress and the use of a battery including the cathode unit according to the invention for power supply.

## Slide 29: APPENDIX 1: SOURCES
https://unstats.un.org/unsd/trade/s_geneva2011/refdocs/RDs/Lithium-Ion%20Batteries%20(Gereffi%20-%20May%202010).pdf
https://www.bcg.com/documents/file36615.pdf
https://www.bcg.com/en-in/publications/2018/future-battery-production-electric-vehicles.aspx
http://www.yole.fr/Li-Ion_BatteryCell_Overview.aspx#.W-bTWJMzbIU
https://www.benzinga.com/pressreleases/17/12/b10968776/world-nmc-lithium-ion-batteries-patent-landscape-report-2017-research-
https://www.businesswire.com/news/home/20180808005396/en/Electric-Bus-Market-China-2013-2018-2025-Analysis
https://markets.businessinsider.com/news/stocks/nmc-lithium-ion-batteries-patent-landscape-1006645170
http://www.crossroadstoday.com/story/39131483/lithium-ion-battery-market-share-size-global-trends-analysis-growth-and-forecast-to-2025
https://www.wikiwand.com/en/History_of_the_electric_vehicle
http://www.visualcapitalist.com/cathode-advancing-lithium-ion/
https://smallcappower.com/community-contribution/community-articles/nickel-price-lithium/
http://www.hitachi.com/
http://www.hitachi-automotive.us/hiams-am.htm
https://www.johnsoncontrols.com/en_hk/batteries
http://www.lgchem.com/global/main

## Slide 30: APPENDIX 2: DEFINITION OF IPC CLASSES
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
IPC CLASS | DEFINITIONS
H01M | Processes or Means, e.g. Batteries, For the Direct Conversion of Chemical Into Electrical Energy
H01M 4/36 | Selection of substances as active materials, active masses, active liquids
H01M 4/525 | of mixed oxides or hydroxides containing iron, cobalt or nickel for inserting or intercalating light metals, e.g. LiNiO2, LiCoO2or LiCoOxFy
H01M 10/052 | Li-accumulators
H01M 10/0525 | Rocking-chair batteries, i.e. batteries with lithium insertion or intercalation in both electrodes; Lithium-ion batteries
H01M 4/62 | Selection of inactive substances as ingredients for active masses, e.g. binders, fillers
H01M 4/13 | Electrodes for accumulators with non-aqueous electrolyte, e.g. for lithium-accumulators; Processes of manufacture thereof
H01M 4/131 | Electrodes based on mixed oxides or hydroxides, or on mixtures of oxides or hydroxides, e.g. LiCoOx
H01M 4/505 | Of mixed oxides or hydroxides containing manganese for inserting or intercalating light metals, e.g. LiMn2O4 or LiMn2OxFy
H01M 10/0585 | Of accumulators having only flat construction elements, i.e. flat positive electrodes, flat negative electrodes and flat separators

## Slide 31: Disclaimer
IIPRD has prepared this sample report as an exemplary report, wherein the content of the report is based on internal evaluation of Patents and Non-Patent Literature that is conducted based on Databases and Information sources that are believed to be reliable by IIPRD. A complete list of patent documents retrieved is not disclosed herein as the report is exemplary but can be shared if desired based on terms and conditions of IIPRD. IIPRD disclaims all warranties as to the accuracy, completeness or adequacy of such information. The above sample report is prepared based on the search conducted on the keywords and other information extracted from the understanding of the Patent Analysts of IIPRD, and subjectivity of the researcher and analyst. Neither IIPRD nor its affiliates nor any of its proprietors, employees (together, "personnel") are intending to provide legal advice in this matter.

## Slide 32: Contact Details
CONTACT DETAILS
Delhi | Noida | Mumbai | Pune | Bangalore | Hyderabad | Indore
US | Bangladesh | Myanmar | Malaysia | Vietnam | Nepal | Sri Lanka
Contact Details
Noida (NCR) Office – Head Office
E-13, UPSIDC Site-IV, Behind Grand Venice, Greater Noida, 201310
Contact Person: Tarun Khurana
Contact No(s):+91-(120) 4296878, 4909201, 4516201
E-Mail: iiprd@iiprd.com, info@khuranaandkhurana.com
Website: www.iiprd.com | www.khuranaandkhurana.com

## Slide 33: About IIPRD
Office- E-13, UPSIDC Site-IV, Behind Grand Venice, Greater Noida, 201308, India ,Phone: +91-(120) 4296878, 4909201, 4516201, Website: www.iiprd.com, Email: iiprd@iiprd.com
IIPRD is a premier Intellectual Property Consulting and Commercialization/Licensing Firm with a diversified business practice providing services in the domain of Commercialization, Valuation, Licensing, Transfer of Technology and Due-Diligence of Intellectual Property Assets along with providing complete IP and Patent Analytics and Litigation Support Services to International Corporate and Global IP Law Firms.